## Slide 1: DEFINING AND MEASURING SUSTAINABILITY
Peter Harper
XX30191 ENERGY AND ENVIRONMENT 2014
Lecture 3

## Slide 2: AN IMPORTANT DISTINCTION
There is a difference between ‘sustainable’ and ‘environmental’
  You can have ‘unsustainable’ national economies, or businesses or health conditions
Many ‘classical’ environmental problems are not ‘unsustainable’ and could continue indefinitely
  Horrible buildings, or wind farms
  Traffic noise and congestion
  Smog, dirty air
  Typical levels of water pollution
  Litter
  Problems of environmental sustainability have boundaries or thresholds, beyond which serious, possibly irreversible, outcomes become more likely, especially in the future
  So sustainability inevitably involves processes over time, where benefits and costs might accrue to different people

## Slide 3: SUSTAINABILITY ENTAILS AN ELEMENT OF TIME OR ‘FUTURITY’ Often across generations
‘Environmental Sustainability’ was approximated as ‘Sustainable Development’ by Brundtland (1987)
SD defined as ‘development that meets the needs of the present without compromising the needs of the future’
This is a good working definition of environmental sustainability
But trying to quantify the ‘needs of the future’ is problematic
“They” are not here to press their case
The definition needs complementing by consideration of the balance of risks to present and future generations

## Slide 4: A CARTOON VIEW OF INTERGENERATIONAL EQUITY On most estimates of the relative costs, successful prevention of climate change looks like a bargain from the perspective of people in the future. But from the present perspective, mitigation costs look dauntingly large and adaptation costs virtually invisible.

## Slide 5: STANDARD ‘B.A.U.’ MODEL OF MITIGATION PROCESSES With principal actors for each component
Outcome (private sector)
Trend identified
(research community/
public sector)
Extrapolated trend
(civil sector)
Mitigation legislation (public sector)
ENVIRONMENTAL IMPACT (NOTIONAL ARITHMETIC SCALE)

## Slide 6: THRESHOLD ADDED TO STANDARD MODEL OF MITIGATION PROCESSES
Outcomes qualitatively different and possibly irreversible
Trend identified
Extrapolated trend
Mitigation measures insufficient or delayed
ENVIRONMENTAL IMPACT (NOTIONAL ARITHMETIC SCALE)
Threshold

## Slide 7: CRITICS ASK
Even if they occur, would such outcomes really be so serious?
Is this extrapolation plausible?
ENVIRONMENTAL IMPACT (NOTIONAL ARITHMETIC SCALE)
Does this threshold really exist?
Is this trend real?
In any case, would it not be cheaper to pay for adaptation?
Can we really give it a reliable value or probability?
These are not certainties, merely possibilities
People in the future will be richer than us, and better able afford the extra costs and risks

## Slide 8
Rockström et al., 2009
‘PLANETARY BOUNDARIES’ (ROCKSTRÖM et al.,2009) A combination of boundary and trend gives an approximate ranking for urgency
Proposed principal thresholds

## Slide 9: THE ECOLOGICAL FOOTPRINT Source: www.wwf.panda.org
Threshold (One Earth)
This is also an example of a highly aggregated indicator
Categories and proportions correlate well with GHGE

## Slide 10: FORTUNATELY DIFFERENT IMPACTS CORRELATE QUITE WELL, MAKING THE PROCESS OF ‘AGGREGATION’ EASIER AND MORE MEANINGFUL Note that ‘global warming’ (GHG emissions) also correlates well with other impacts, suggesting its use as an easily-measured ‘proxy’ in certain circumstances

## Slide 11: THE CASE OF CLIMATE CHANGE HOW SHOULD WE SET THRESHOLDS? AN UNCOMFORTABLE MIXTURE OF SCIENCE, ETHICS AND POLITICS
http://www.pnas.org/content/106/11/4133.full
“Dangerous”
“Very dangerous”
“Extremely dangerous”

## Slide 12: EMISSION OF GHGs (GHGE) IS A GOOD ‘PROXY’ FOR AN AGGREGATED MEASURES OF ENVIRONMENTAL IMPACTS
Aggregating diverse measures is methodologically awkward
GHGE ‘footprint’ methodology is correctly additive
GHGE correlates well with other measures
  Possibly a measure of ‘technological brute force’
A good approximation to the ‘Ecological Footprint’
GHGE can be relatively easily and precisely measured at any level, generating single, meaningful values and revealing trends
GHGE can usually be compared against measurable thresholds to indicate urgency and importance
Climate change is a major problem that must be solved, or most other environmental problems become irrelevant

## Slide 13: MAIN MEASURES FOR CLIMATE CHANGE
Rate of emissions
Level of GHGs in atmosphere
Actual forcings of temperature
Temperature rise
Probabilities of certain outcomes
Cumulative emissions and ‘Carbon Budgets’

## Slide 14: GHG EMISSIONS (GHGE)
Not all CO2
Kyoto ‘basket’
  CO2, CH4, N2O, CFCs, SF6, others
Some argument about how to add them up
Usually 100-year equivalent to CO2in terms of Global Warming Potential (GWP)
Unit is CO2e
Usually expressed as a rate, e.g., MtCO2e/y
Present world level ~45 GtCO2e/y
Proposed sustainable level zero by 2050?

## Slide 15: RELATIVE WORLD EMISSIONS OF CO2 AND NON-CO2 GHGS

## Slide 16: CONCENTRATION OF GHGs IN ATMOSPHERE
Not all GHGE end up in the atmosphere
  Almost half goes into oceans and biomass
But the two are obviously related
Usually measured in ppm of CO2 or total GHG in equivalents CO2e
Pre-industrial level 270 ppm, measured now 400 ppmCO2
Targets proposed: 550, 450, 350 ppm

## Slide 17: ACTUAL ‘FORCINGS’: NOT ALL DUE TO GHG
Usually measured in Watts per square metre
Ultimate target: net zero
Source: IPCC AR5 (2013)

## Slide 18: ATMOSPHERIC TEMPERATURE
Not so very easy to measure
  Many different methods and sample points required
‘Sensitivity’ to forcing remains uncertain
Current level around 0.8ºC above baseline
This generates measurable and noticeable effects
Risks of knock-on effects and ‘non-linear responses’ are thought to rise sharply above 2ºC
2ºC is considered the working threshold for ‘dangerous climate change’ that must not be exceeded
Current forcing trends would lead to 3º-4ºC if maintained

## Slide 19: PROBABILITIES
Processes and outcomes cannot be exactly determined or predicted
Probabilities are assigned on the basis of modelling and informed estimates
They are subject to review and modification with new data and understandings
Scenarios and policy measures are commonly evaluated in terms of their probability of exceeding the 2ºC threshold
Level of risk-taking is a political or ethical matter, not a scientific one
Likelihood Terminology | Likelihood of the occurrence/ outcome
Virtually certain | > 99% probability
Extremely likely | > 95% probability
Very likely | > 90% probability
Likely | > 66% probability
More likely than not | > 50% probability
About as likely as not | 33 to 66% probability
Unlikely | < 33% probability
Very unlikely | < 10% probability
Extremely unlikely | < 5% probability
Exceptionally unlikely | < 1% probability
Source IPCC AR4, 2007

## Slide 20: THE PRINCIPLE OF CUMULATIVE EMISSIONS
Many GHGs remain in the atmosphere for a long time
This is a big difference from most ‘classical’ environmental problems, that are self-correcting once the inputs stop
Reduction targets and dates for GHG reduction are not enough to guarantee reduced concentrations
Total accumulated emissions becomes a key metric
This can be related to a global ‘carbon budget’ to guide policy, that can be expressed in GtCO2e, approximately equivalent to “450ppm”

## Slide 21: The principle of calculating default cumulative emissions tCO2e/y*y = tCO2e 637*20/2 = 6370MtCO2e
Area under the curve
127
127*40+(637-127)*40/2
15296

## Slide 22: BUT THE TRAJECTORY IS NOT NECESSARILY LINEAR. ITS SHAPE CAN MAKE A LARGE DIFFERENCE TO THE ACCUMULATED EMISSIONS

## Slide 23: ‘CARBON BUDGETS’ OR ALLOWABLE EMISSIONS QUOTAS CAN BE ALLOCATED TO COUNTRIES ON THE BASIS OF EQUAL PER CAPITA ENTITLEMENT
GERMAN ADVISORY COUNCIL ON GLOBAL CHANGE
YOU CAN CHOOSE HOW AND WHEN TO ‘SPEND’ YOUR CARBON ALLOWANCE, BUT HIGH EMITTERS HAVE TO MOVE FASTER

## Slide 24: CALCULATING THE UK’S SUSTAINABLE EMISSIONS ENTITLEMENT FROM GLOBAL ESTIMATES OF A ‘BUDGET’ THAT WOULD GIVE 20% CHANCE OF EXCEEDING 2ºC Is this probability unreasonable? Too high? Too low?
AEQ PERIOD | World Quota, GtCO2e | World average population, millions | Per cap quota, tCO2e | Global Per cap per year | UK average population, millions | UK pro rata quota, GtCO2e | UK average quota per year, MtCO2e
1990-2050 | 1722 | 7297 | 236.0 | 3.9 | 68.08 | 16.1 | 268
2000-2050 | 1356 | 7947 | 170.6 | 3.0 | 69.15 | 11.8 | 236
2010-2050 | 894 | 9510 | 107.1 | 2.7 | 70.17 | 7.5 | 188
2015-2050 | 643 | 8729 | 75.4 | 2.2 | 71.19 | 5.4 | 153

## Slide 25: THERE REMAINS A PROBLEM OF WHICH UK EMISSIONS TO COUNT
Should we count only the emissions that are generated in the UK itself?
Or should we count all emissions associated with UK consumption, outside the UK?
  If we don’t count these in, who does?
Should the allocation period start at some agreed point in the future?
Or should it include some measure of ‘historical responsibility?
  If we don’t count these in, who does?

## Slide 26: UK official policy, target, results
Notes: We chose 2030 as a date by which we belive this is technically feasible

## Slide 27: Which emissions should we count?
Notes: We chose 2030 as a date by which we belive this is technically feasible

## Slide 28
Chart: UK GHGE MtCO2e/y
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
CO2 | 578 | 554 | 554 | 534 | 490 | 460 | 400 | 350 | 260 | 190 | 140 | 120 | 92
OTHER GHG | 164.8 | 139.6 | 111.2 | 94.6 | 100 | 90 | 79.7143 | 69.4286 | 45 | 34.7143 | 35 | 25 | 18
UK ACCUMULATED EMISSIONS
ALLOWABLE EMISSIONS QUOTA

## Slide 29
Chart: UK GHGE MtCO2e/y
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
CO2 | 578 | 554 | 554 | 534 | 490 | 460 | 400 | 350 | 260 | 190 | 140 | 120 | 92
OTHER GHG | 164.8 | 139.6 | 111.2 | 94.6 | 100 | 90 | 79.7143 | 69.4286 | 45 | 34.7143 | 35 | 25 | 18
ENV ACC | 42.7569 | 58.794 | 63.4227 | 74.9117 | 56.6914 | 45 | 39.8571 | 34.7143 | 29.5714 | 24.4286 | 19.2857 | 14.1429 | 9
CONS | 72.4431 | 134.006 | 240 | 300 | 320 | 270 | 239.1429 | 208.2857 | 177.4286 | 146.5714 | 115.7143 | 84.8571 | 54
ILUC | 101 | 101 | 101 | 101 | 101 | 101 | 89.4571 | 77.9143 | 66.3714 | 54.8286 | 43.2857 | 31.7429 | 20.2

## Slide 30: ‘COMPREHENSIVE’ EMISSIONS FRAME FOR THE UK?

## Slide 31: UK EMISSIONS ABOVE QUOTA FOR VARIOUS FRAMES Either ‘physics’ or ‘fairness’ must give way, possibly both, making international agreement difficult
 | Excess emissions above equal per-capita quota for 80% chance of remaining under 2ºC, MtCO2e. 2010 UK territorial emissions ~600M/y |  |  |  | 
AEQ PERIOD | 1. CO2 only | 2. All GHG ‘Territorial account’ | 3. + international transport ‘Production account’ | 4. + emissions embodied in net imports ‘Consumption account’ | 5. +Land use ‘Com-prehensive account’
1990-2050 | 7594 | 12985 | 15890 | 28034 | 32326
2000-2050 | 6201 | 10070 | 12257 | 22773 | 26055
2010-2050 | 5043 | 7883 | 9423 | 16096 | 18369
2015-2050 | 5270 | 7080 | 8595 | 13638 | 15406

## Slide 32: THIS IS JUST THE CLIMATE CHANGE ASPECT
The current young generation will also have to deal with land use, the food system, production of goods.
It is helpful to have a physically realistic model of the problems and programmes to engage them
But there is a big gap between physical and political ‘realism’

## Slide 33
THE YAWNING CHASM
POLITICAL REALISM
PHYSICAL REALISM
FURIOUS ACTIVITY
ZCB etc

## Slide 34
Credit: © Stapleton Historical Collection / Heritage-Images / Imagestate
Well guys, it looks as if we have a result
Physics Trumps Politics
Get the physics right, then adjust the politics and economics: NOT the other way round

## Slide 35: CONSIDERATION OF THE WIDE GAP BETWEEN PHYSICAL REQUIREMENTS AND THE LIKELY POLITICAL RESPONSE SUGGESTS A BIFURCATION OF THE HISTORICAL TRAJECTORY
COSTS, RISKS, EFFORT, AND GENERAL UNPLEASANTNESS
TIME, 21ST CENTURY
THE ‘PHYSICALIST’ VIEW
Applying necessary adjustments and living with some limitations maintains as much as possible of the status quo
THE ‘POLITICAL’ VIEW
Insistence on maintaining the status quo eventually destroys it

## Slide 36: THE END