## Slide 1: ENERGY: FAIRNESS,PHYSICS AND SUSTAINABILITY
Peter Harper
University of Bath
Centre for Alternative Technology

## Slide 2
Credit: © Stapleton Historical Collection / Heritage-Images / Imagestate
Well guys, it looks as if we have a result
Physics Trumps Politics

## Slide 3: THE CHURCHILL PRINCIPLE

## Slide 4
THE YAWNING CHASM
POLITICAL REALISM
PHYSICAL REALISM
FURIOUS ACTIVITY
ZCB etc

## Slide 5: “SUSTAINABILITY” NEEDS QUANTIFYING” ‘GLOBAL WARMING’ ≈ GHG EMISSIONS A GOOD PROXY MEASURABLE AND CONSERVED

## Slide 6: GHG EMISSIONS MOSTLY RELATED TO ENERGY -- BUT NOT ALL

## Slide 8: THE UK’S NON-CO2 EMISSIONS

## Slide 9: PROJECTIONS OF NON-CO2 GHGs TO 2050
Methane GWP now considered 36% higher than previously (IPCC)
22% population growth needs proportionately more agricultural production
UK economy expected to grow at 2.1%/yr: double present by 2050.
Waste & demand for non-energy services unlikely to be unaffected

## Slide 10
YOU WOULD HAVE TO GET YOUR ENERGY OUT OF THIS BIT
NON-ENERGY EMISSIONS

## Slide 11: PROBING 2050 ENERGY EMISSIONS
 | Population p | GDP/cap g | Energy Intensity e | Carbon Intensity f | Total p*g*e*f (Target <50)
 | N x 10^6 | £/N X 10^3 | kWh/£ | kgCO2e/kWh | MtCO2e

## Slide 12: TYPICAL PATTERN OF ENERGY INTENSITY OVER TIME ENERGY/UNIT GDP

## Slide 13: PROBING 2050 ENERGY EMISSIONS
 | Population p | GDP/cap g | Energy Intensity e | Carbon Intensity f | Total p*g*e*f (Target <50)
 | N x 10^6 | £/N X 10^3 | kWh/£ | kgCO2e/kWh | MtCO2e

## Slide 14: CARBON INTENSITIES OF ENERGY SYSTEMS Data from IPCC, 2013
Chart: CARBON INTENSITY OF ENERGY SUPPLY SYSTEMS, kgCO2e/kWh
| Coal to electricity | Gas to electricity | Biomass electricity | Coal with CCS | Gas with CCS | Coal CCS wih biomass | Geothermal | PV | Nuclear | Concentrating solar | Offshore wind | Onshore wind | Hydro | Wave and tidal | Gas for heating | Biomass for heating | Solar thermal | Oil (transport) | Biofuels for transport
 | 1 | 0.46 | 0.2 | 0.2 | 0.17 | 0 | 0.045 | 0.045 | 0.016 | 0.022 | 0.02 | 0.015 | 0.004 | 0.02 | 0.2 | 0.02 | 0.022 | 0.3 | 0.15
ELECTRICITY
HEAT
TRANSPORT

## Slide 15: PROBING 2050 ENERGY EMISSIONS
 | Population | GDP/cap | Energy Intensity | Carbon Intensity | Total (Target <50)
2010 | N x 10^6 | £/n X 10^3 | kWh/£ | kgCO2e/kWh | MtCO2e
Base case | 62 | 23 | 1.28 | 0.27 | 493

## Slide 16: PROBING 2050 ENERGY EMISSIONS
 | Population | GDP/cap | Energy Intensity | Carbon Intensity | Total (Target <50)
2010 | N x 10^6 | £/n X 10^3 | kWh/£ | kgCO2e/kWh | MtCO2e
Base case | 62 | 23 | 1.28 | 0.27 | 493
2050 |  |  |  |  | 
‘BAU’ at 2.1% | 77 | 44.7 | 0.93 | 0.20 | 641

## Slide 17: PROBING 2050 ENERGY EMISSIONS
 | Population | GDP/cap | Energy Intensity | Carbon Intensity | Total (Target <50)
2010 | N x 10^6 | £/n X 10^3 | kWh/£ | kgCO2e/kWh | MtCO2e
Base case | 62 | 23 | 1.28 | 0.27 | 493
2050 |  |  |  |  | 
‘BAU’ | 77 | 44.7 | 0.93 | 0.20 | 641
1% growth | 77 | 29 | 0.93 | 0.20 | 415

## Slide 18: PROBING 2050 ENERGY EMISSIONS
 | Population | GDP/cap | Energy Intensity | Carbon Intensity | Total (Target <50)
2010 | N x 10^6 | £/n X 10^3 | kWh/£ | kgCO2e/kWh | MtCO2e
Base case | 62 | 23 | 1.28 | 0.27 | 493
2050 |  |  |  |  | 
‘BAU’ | 77 | 44.7 | 0.93 | 0.20 | 641
1% growth | 77 | 29 | 0.93 | 0.20 | 415
E Intensity only | 77 | 29 | 0.115 | 0.20 | 50

## Slide 19: HOW MUCH ENERGY WILL WE USE IN 2050? EXTRAPOLATE THE LAST 40 YEARS INTO THE NEXT 40?
We are running at about 4kW a head.
Can we imagine running at about 0.5kW?

## Slide 20: PROBING 2050 ENERGY EMISSIONS
 | Population | GDP/cap | Energy Intensity | Carbon Intensity | Total (Target <50)
2010 | N x 10^6 | £/n X 10^3 | kWh/£ | kgCO2e/kWh | MtCO2e
Base case | 62 | 23 | 1.28 | 0.27 | 493
2050 |  |  |  |  | 
‘BAU’ | 77 | 44.7 | 0.93 | 0.20 | 641
1% growth | 77 | 29 | 0.93 | 0.20 | 415
E Intensity only | 77 | 29 | 0.0115 | 0.20 | 50
C intensity only | 77 | 29 | 0.93 | 0.024 | 50

## Slide 21: CARBON INTENSITIES OF ENERGY SYSTEMS Data from IPCC, 2013
Chart: CARBON INTENSITY OF ENERGY SUPPLY SYSTEMS, kgCO2e/kWh
| Coal to electricity | Gas to electricity | Biomass electricity | Coal with CCS | Gas with CCS | Coal CCS wih biomass | Geothermal | PV | Nuclear | Concentrating solar | Offshore wind | Onshore wind | Hydro | Wave and tidal | Gas for heating | Biomass for heating | Solar thermal | Oil (transport) | Biofuels for transport
 | 1 | 0.46 | 0.2 | 0.2 | 0.17 | 0 | 0.045 | 0.045 | 0.016 | 0.022 | 0.02 | 0.015 | 0.004 | 0.02 | 0.2 | 0.02 | 0.022 | 0.3 | 0.15
ELECTRICITY
HEAT
TRANSPORT

## Slide 22: PROBING 2050 ENERGY EMISSIONS
 | Population | GDP/cap | Energy Intensity | Carbon Intensity | Total (Target <50)
2010 | N x 10^6 | £/n X 10^3 | kWh/£ | kgCO2e/kWh | MtCO2e
Base case | 62 | 23 | 1.28 | 0.27 | 493
2050 |  |  |  |  | 
‘BAU’ | 77 | 44.7 | 0.93 | 0.20 | 641
1% growth | 77 | 29 | 0.93 | 0.20 | 415
E Intensity only | 77 | 29 | 0.0115 | 0.20 | 50
C intensity only | 77 | 29 | 0.93 | 0.024 | 50
E at 60% present | 77 | 29 | 0.760 | 0.029 | 50

## Slide 23: DAVID MACKAY’S LOW-CARBON SCENARIOS Proposed by David Mackay, Sustainable Energy Without The Hot Air, 2008

## Slide 25: DAVID MACKAY’S SCENARIOS G AND E Can they work in 2050?

## Slide 26: THE BRUTAL PHYSICS
Tells us that, with the exception of limited biomass CCS co-firing, UK commitments cannot be met with more than a very small fraction of fossil fuels, even with widespread CCS
The choices are (mix ‘n match) between
  Energy intensity
  Nuclear
  Renewables
It’s very electric
  More grid, more pylons

## Slide 28: UNFORTUNATELY, UNLIKE MOST OTHER POLLUTANTS, GHGs DON’T GO AWAY QUICKLY It’s not targets that count: it’s cumulative emissions

## Slide 29: WHAT IS THE SUSTAINABLE LEVEL? AND WHAT IS A FAIR QUOTA FOR EACH PERSON OR NATION?
Less than 20% chance of exceeding 2°C
  Is this reasonable?
Allowable emissions 2015-2050 for this level of risk, about 643 GtCO2e
Allocate on an equal per capita basis?
Say average of 8.5 billion people in this period, 76 tCO2 each, 2.2 t per person year
This allocation falls after each year if it is exceeded, but gives us a rough benchmark

## Slide 30: WHAT IS BRITAIN’S SHARE OF THE GLOBAL BUDGET?
AEQ PERIOD | World Quota, GtCO2e | World average population, millions | Per cap quota, tCO2e | Global Per cap per year | UK average population, millions | UK pro rata quota, GtCO2e | UK national quota per year, MtCO2e
1990-2050 | 1722 | 7297 | 236.0 | 3.9 | 68.08 | 16.1 | 268
2000-2050 | 1356 | 7947 | 170.6 | 3.0 | 69.15 | 11.8 | 236
2010-2050 | 894 | 8510 | 107.1 | 2.7 | 70.17 | 7.5 | 188
2015-2050 | 643 | 8729 | 75.4 | 2.2 | 71.19 | 5.4 | 153

## Slide 31: APPLYING THE BENCHMARK TO THE UK
Less than 2 tCO2e/head

## Slide 32: WOULD BOLDER, FASTER TARGETS HELP? Yes, a bit.

## Slide 33: A QUICK PLUG FOR ZERO-CARBON BRITAIN A non-fossil, non-nuclear scenario that keeps the lights on
Notes: What we see here is the energy flow diagram for our scenario.
On the right hand side we see all the ways how we use energy – heating, appliances, industry, transport, what we’ve just discussed.
And on the left hand side we see the renewable energy sources that we use.
This is based on a thorough literature review and analysis of how much renewable energy we can produce in the UK from different sources.
So we’ve looked at how many offshore wind farms we can build, what percentage of all UK roofs we can cover in solar panels, how much wave and tidal power we can realistically harvest, to make sure that we meet the demand.
I don’t want to go into the details but just three observations:
We produce enough energy
Wind power is by far the biggest contributor – the UK has a fantastic wind resource, especially offshore
Most energy is produced and delivered as electricity
33

## Slide 34: FAIRNESS WHICH EMISSIONS SHOULD WE COUNT?
Notes: We chose 2030 as a date by which we belive this is technically feasible

## Slide 35: ALL EMISSIONS POTENTIALLY ATTRIBUTABLE TO THE UK, 1990-2050 Based on data from a study at the University of Leeds
Chart: UK GHGE MtCO2e/y
| 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
CO2 | 578 | 554 | 554 | 534 | 490 | 460 | 400 | 350 | 260 | 190 | 140 | 120 | 92
OTHER GHG | 164.8 | 139.6 | 111.2 | 94.6 | 100 | 90 | 79.7143 | 69.4286 | 45 | 34.7143 | 35 | 25 | 18
ENV ACC | 42.7569 | 58.794 | 63.4227 | 74.9117 | 56.6914 | 45 | 39.8571 | 34.7143 | 29.5714 | 24.4286 | 19.2857 | 14.1429 | 9
CONS | 72.4431 | 134.006 | 240 | 300 | 320 | 270 | 239.1429 | 208.2857 | 177.4286 | 146.5714 | 115.7143 | 84.8571 | 54
ILUC | 101 | 101 | 101 | 101 | 101 | 101 | 89.4571 | 77.9143 | 66.3714 | 54.8286 | 43.2857 | 31.7429 | 20.2
Allowable quota

## Slide 36: ‘COMPREHENSIVE’ EMISSIONS FRAME FOR THE UK?

## Slide 37: WHAT DOES ALL THIS MEAN?
Little Britain cannot save itself, much less the Planet, on its own
It cannot even pay its ‘carbon debts’ from its own territorial resources
It has to engage actively in a worldwide decarbonisation process
Most of this will be energy systems, with food and land use, and enhanced carbon sinks, playing a significant role
A bigger vision will be necessary, but it’s possible, and it could be really exciting

## Slide 40: ALTERED RESEARCH PRIORITIES
Suspend space, particle physics → 22nd century (!!!)
Minimise need for supply by maximising energy services (efficiency/energy intensity)
Accelerated R&D in all fields of renewable energy
Energy carriers: hydrogen, e-methane, urea etc
Energy storage: batteries, thermal, cryogenic etc
Benign geoengineering: CCS, BECCS, air capture
Facilitate low-carbon lifestyles

## Slide 41: A RAPID GLOBAL TRANSFORMATION Driven by fairness, physics and sustainability
Unlikely?
Canute and Churchill agree it’s necessary
It would be rather like a war
  Because we’ve left it to the last minute
  But entirely winnable
Costs are largely irrelevant
  But it might well be financially beneficial
UK and international diplomacy vital
  The carbon attaché
  Robust systems of international carbon credits to promote transfers
Escalating international carbon price
  Removal of subsidies for fossil fuels
Leave fossil fuels in the ground
  No fracking, no further oil exploration
  Encourage fossil companies to move into renewables

## Slide 42: WHICH EGGS SHOULD BE BROKEN? These:
Higher cost
Lower energy consumption
Lots of wind, both on- and off-shore
Tidal power
Bioenergy
‘Benign geoengineering’
International energy/carbon investments
Less flying, less meat consumption

## Slide 43
CALLING A SPADE A SPADE:
GROWN-UP DEBATES ABOUT ENERGY
Keep it cheap!
No Power Cuts!
LOTS of it!
...AND NO OFFSETS!
...OR CARBON CAPTURE AND STORAGE!
...OR GEO-ENGINEERING!
...OR BIOFUELS!
...OR LIFESTYLE CHANGES!